## Slide 1: A GNURADIO-based Software Defined GPS Receiver
EECS 498 Course Project Final Presentation
Dinan Bai, Tianyu Yin

## Slide 2: Content
GPS Background & Theory
GNUradio-based GPS receiver Design & Validation
Experiment
  Our real in-situ Measurement in Ann Arbor
Conclusion

## Slide 3: 1. GPS Background
GPS Application: Navigation
Source: https://spaceplace.nasa.gov/gps/en/
Positioning a receiver
Idea behind it
  We want to solve for x, y, z for a location
  It requires at least 3 satellites locations & delay of signal propagation (If considering time bias, then need 4)
  Each satellite transmits its ephemeris info to ground receiver
  Ground receiver parses the ephemeris info and calculates its position

## Slide 4
1ms
1ms
20ms, 20 PRN cycles for 1 navigation bit
GPS transmits message bits: BPSK, 50 bps, or 1 bit for 20 ms
However, due to channel effects …
  Delay
  Doppler frequency shift
  Noise
we need to estimate timing/frequency (recall what we learned in class!) at the receiver to correctly receive GPS message bits
Use Pseudo Random Noise (PRN) codes!
  32 GPS satellites are assigned with their own PRN code (e.g. PRN 1, PRN 2, … , PRN 32)
  Different PRNs are orthogonal
In this project, we focus on the L1 band C/A code
PRN
PRN

## Slide 5
2. Receiver Design Overview
Received signal
Acquisition
Tracking
Navigation
What we did
How many PRNs can be detected?
Where are they? (delay & doppler)
Takes a long time (cold start)
Track the navigation bits at the estimated delay & doppler
Since we know them in the acquisition stage, it’s going to be fast

## Slide 6
a. PRN code – L1 civil ranging code
C/A Code – Gold Code
One cycle: 1023 bits
Chipping rate: 1023 Kbps
Every cycle lasts 1 ms
Source: IS-GPS-200D

## Slide 7
b. Acquisition – Delay Doppler Map:
Goal: find received signal peak delay & doppler
Math:
  Received & sampled signal , local PRN
  Delay Doppler Map =
  Peak of corresponds to the estimated delay & doppler frequency
Notes: We got. A received signal and local PRN
Then we can do a cross-correlation between received signal, and a time delay & freq shift version of local PRN
A delay doppler map is formed e.g. the figure
The magnitude peak in the ddm corresponds to the estimated delay and doppler frequency

## Slide 8
b. Acquisition – Time-lag Correlation:
Fix at a frequency, e.g.
Cross-correlation:
-- Circular Convolution, Time complexity
PRN
PRN
PRN
1 ms signal
Equivalently, Circular Convolution! Then we can use FFT
PRN
1 ms signal
Equivalent with FFT, Time Complexity :
Notes: Lets examine the time-lag correlation with a fixed frequency shift
Correlation is equivalent to convolution, but one of them is time reversed and conjugated
A simple way is to shift one signal by one bit delay, then calculate correlation, then next bit. When they are lined up, the correlation peaks and delay is found. In this way, the time complexity is o n2
Due to the periodicity equivalently this is a circular convolution
So we can apply FFT, the correlation is mathmatcially equivalent to
And the time complexity is o nlogn, becomes much faster when data amount is huge

## Slide 9
b. Acquisition – FFT based cross-correlation
Time-lag Correlation Waveform
Notes: Gnuradio structure to realize the FFT-based xcorr
Hierarchy block
Input -- output

## Slide 10
7-thread-parallel search of correlation
Why 7? Because my computer has 8 cores
Correlation based on shift: 10s for one PRN search
Correlation Based on FFT: 2 s for 32 PRNs
Notes: Parallel the doppler search:
7 threads
Each output is a delay cut – if we take 4 samples per bit, the ddm size will be 7*1023*4. peak search
speed

## Slide 11
c. Frequency Coarse & Fine Search
500 Hz Bandwidth
Ambiguity function frequency cut
Coarse search:
First round: [-1500,-1000, -500, 0, 500, 1000, 1500] Hz
Not found?
Second: centered at 3500 Hz, 2000 to 5000 Hz
Third, negative of Second round frequency
In the end, at most 5 rounds search, cover -8.5 to 8.5 KHz
Still not found? Give up and move to the next PRN
Fine search:
If peak is found, center at the peak frequency
Change new to be
After 6 rounds iteration, resolution reaches ~1Hz
Tracking:
If the peak and doppler frequency are known, then in the tracking stage, we can shrink the search range
Delay & doppler change slightly and continuously in time

## Slide 12
d. Validation1 – Simulation:

## Slide 13
d. Validation 2 – Airborne GPS IF band data testing
IF band – Intermediate Frequency band (4.1304MHz)
IF band IQ sampled and down-converted to baseband
IF band spectrum
Baseband spectrum

## Slide 14
Compare the detected PRN with the reference result
  Determine the peak detection threshold
  Achieved 100% accuracy in PRN detection correctness
  E.g. PRN 2
Notes: For example, the receiver detected PRN2
the delay and doppler frequency correlation waveform (2d cuts along delay and doppler axis which contains the peak)
We need to find a way to find the peak and determine whether it’s a valid peak

## Slide 15
(Correlation Output)
Peak Detection Threshold
SNRm (mean value SNR) =
SNRs (std SNR) =

## Slide 16
3. In-situ GPS Signal Measurement Experiment
USRP
NUC2 Computer
Active Antenna
With its ground plane
UPS Power Source
DC Supply

## Slide 17
Bias TEE
Active Antenna

## Slide 18
PRNs we found… PRN 2, PRN 14, PRN 30

## Slide 19
Navigation Satellite Positions at 12/7/2024, 17:15pm Eastern Time
PRN 14

## Slide 20
Tracking Results:
Tracking PRN 2: 1s data, 1000 code cycle tracking
Gaussian like distribution
Delay
Doppler
Phase
SNRm

## Slide 21
Tracking a PRN that is not detected
Uniform distribution
Delay
Doppler
Phase
SNRm

## Slide 22
4. Conclusions
We built a USRP-Gnuradio based GPS receiver
In the experiment, we managed to detect and track GPS satellite PRNs
However, we do not have enough time to do the remote sensing application
Also, the system is not suitable for remote sensing application
Discussion: The USRP received signal is very noisy compared with other GPS receivers
  Noise figure might be too high – the system injects extra noise to the signal (filter, mixer, LNA…)
  Phase noise is too high – Local oscillator is not good

## Slide 23
Q & A

## Slide 24: Tracking
Given the estimate delay and doppler in the 1st ms xcorr, the receiver knows where the signal is
Use phase lock loop (PLL), frequency lock loop (FLL), delay lock loop (DLL) to lock on the signal
  They are feed back loops to the local oscillator & correlation delay & phase shifter
  Use a cost function to estimate their bias, use PI control to feedback
  Adjust the delay, doppler, phase in the next loop
  Cold starts search for N delay * M doppler space, tracking only do 3 delay and 1 frequency search
  This achieves real-time tracking
Phase lock? The carrier phase changes continuously, so we will see rotation in constellation plot. To parse the bpsk modulation of navigation bit correctly, we need to compensate the phase.

## Slide 25
One period: 1023 bits
Chipping rate: 1023 Kbps
Every period lasts 1 ms
PRN code – L1 civil ranging code
C/A Code – Gold Code